## Slide 1
What is it and how can it be implemented?
Sphere technical chapter on shelter, settlements and non-food items (NFIs)
Module A16 – Sphere Training Package 2015
The materials in this presentation have been adapted from the InterWorks technical Sphere course which can be found online at interworksmadison.com

## Slide 2: Shelter, Settlement and NFIs problems
Photo: EPA / Red Cross International
People standing amid the rubble of collapsed houses in Port-au-Prince, Haiti, after a massive 7.0 magnitude earthquake struck the country.
Notes: Even though shelter and site issues are complex and very contextually dependent, there do seem to be recurring problems and issues that site planners and emergency shelter program planners have learned from field experience. The Sphere materials in this chapter represent some of the more agreed-upon findings from many situations around the world.
10 Problems with emergency settlements, camps, shelters, & NFIs
1. No resources for site and shelter
2. Conflicts about location, priorities, and design
3. Exposure to elements while waiting for materials
4. Difficult site conditions
5. Short term solutions to long term problems
6. Constant site work
7. Overcrowding, spread of disease
8. Rape
9. Failure to build or occupy emergency shelter
10. Distributed items (NFI) are not used or don’t last

## Slide 3: Problem 1: No resources for site and shelter
Wassem Al Bakr, Iraqi Red Crescent
Notes: Photo caption: Iraq. 2014. The Khanke IDP camp in Iraq’s Dohuk has become the home of more than one thousand Iraqi families who were forced to leave their towns and cities behind due to the worsening security situation.

## Slide 4: Problem 2: Conflicts about location, priorities and design
Notes: Often different organizations provide different tents and shelter types.
Additionally many different organizations have very different approaches to providing emergency shelter.
While is it useful to discuss options and approaches, time lost in solving conflicts can sometimes slow down the overall response. Furthermore, when significantly different approaches and shelter types are provided to a single community, there may be conflict between those receiving materials perceived to be of greater value by the community and those receiving less.

## Slide 5: Problem 3: Exposure to elements while waiting for materials
Alanah Torralba/IFRC freelance
Notes: Photo caption: Typhoon Haiyan. Philippines. November 2013. A view of a village in Palo, Leyte, Philippines on 13 November 2013

## Slide 6: Problem 4: Difficult site conditions
Camp Hope – June 1999

## Slide 7: Problem 5: Short-term solutions to long-term problems

## Slide 8: Problem 6. Constant site work
Notes: The problem with many new camps is that they are located on poorly chosen sites with inadequate drainage.
This usually means that site work must be done to correct problems that become apparent once the people have already settled.
This type of work often further displaces residents of the camp, and brings mud in wet weather and irritating dust in dry weather.
Both mud and dust cause and complicate many public health issues such as upper respiratory infections from dust and spread of unsanitary conditions leading to increased incidences of diarrhoeas in the case of mud.
While some site work is normal, ongoing and constant repairs and corrections of drainage problems usually mean that the site was not adequate in the first place or initial site planning work was incorrectly designed, or there was not enough money to do what was needed in the initial instance.

## Slide 9: Problem 7: Overcrowding, spread of disease
IFRC/JOSE Manuel Jimenez
Notes: Photo caption: Haiti. 2010. Tarpaulin shelters in La Couronne camp.

## Slide 10: Problem 8: Rape
Women collecting firewood. Photo: Tribune India

## Slide 11: Problem 9: Failure to build or occupy replacement or relocation shelters
Rwanda. Photo: One World

## Slide 12: Problem 10: Distributed items (NFI) not used or don’t last
Olivier Matthys/IFRC
Notes: Photo caption: Pakistan. 2011. Survivors of Pakistan's monsoon floods began the long trek back to their villages in the Kandiah valley, carrying parts of a shelter kit.

## Slide 13: The relationships between the components of the Sphere handbook

## Slide 14: Visualising some indicators and guidance notes…
You know them… but can you see them?

## Slide 15: Some key indicators for shelter
  The initial covered floor area per person is at least 3.5 m2
  The covered area enables safe separation and privacy between the sexes, different age groups, and separate families
Using the Sphere guidelines, what would be a basic planning figure for space per person in a mass shelter like this?
Photo: UNHCR

## Slide 16: Using the indicators in practice
Approx. 1.87 meters
3.5 m2
Approx. 1.87 meters

## Slide 17: Using the indicators in practice
“One program is based on the planning assumption that an average household of 5 people should receive at least one 4 metre x 5 metre sheet of plastic.”
What does this mean in practice?
  4m x 5m = 20m2
  20m2  5 people = 4.0m2 per person
But isn’t that greater than 3.5m2 – the Sphere indicator?
No. But why not?
4m
5m
  20m2
Notes: The answer is provided on the next slide.

## Slide 18: Covered shelter space
4m
5 m
A = ± 2.6 m2/p
4m
2.5 m
32.5m
A = ± 3.0 m2/p
4m
A = ± 3.4 m2/p
5 m
It all depends on context, climate, tradition, and how you use it! The indicator is for covered shelter space, not sq. m. of plastic sheeting distributed!

## Slide 19: People need a new place to live, even if only temporarily. Where do you start?
UNHCR photo

## Slide 20: Site selection and planning – usable area
Some guidance notes on usable area…
“For camp-type settlements, a minimum usable area of 45m2 for each person including household plots should be provided.”
(page 257 of the 2011 Edition)
What exactly does this mean, and where or when does it apply? Can it be less?
Notes: Care should be used in the application of the Guidance note calling for 45m2 per person for a camp site. The number as a guide is only to be used in the initial instance of allocating land for a site to be developed into a camp. In practice each person does not receive 45m2 for their own use as this planning figure includes all of the land required for roads, circulation areas, paths, public administrative and service areas as well as the individual plots for each family’s shelter. The result is that a camp can be planned using this figure that is not overcrowded, and allows for incorporation of all required support services. Once the site is obtained, the figure can also be used to advise planners how many people should be settled at a particular site, however it has no bearing on the final details of the site planning or the amount of land allocated for each individual person or family. In short, it is a gross planning figure only to be used for obtaining a site big enough to plan an adequate camp for a given population size.
Many people are ‘blind’ to the actual reality of these kinds of planning numbers. You can illustrate the area of 45m2 in a classroom space or out of doors with a simple measuring tape. Ask 4 participants to act as ‘corner posts’, and use a meter tape to place them at the four corners of a rectangle 5m wide by 9 meters long. This area is 45 m2.

## Slide 21: Site selection and planning – site gradient
Some guidance notes on site gradient…
“The site gradient should not exceed 5 percent, unless extensive drainage and erosion control measures are taken, or be less than 1 percent to provide for adequate drainage.”
(page 256 of the 2011 Edition)
What exactly does this mean, and where or when does it apply? Can you visualise it?

## Slide 22: Site gradient
  Percent slope is not about degrees.
  Percent slope is the ratio of the change in elevation between two points and the horizontal distance between them.
  In short, elevation change divided by the distance between the two points.
100m
20m
20% slope
Too steep!
100m
10m
10% slope
Too steep!
100m
1- 5m
1-5 % slope
Just right!
100m
0-1m
0-1 % slope
Too flat!

## Slide 23: Site size
Q. How big should a site be to host 20,000 displaced people in an emergency camp?
A. Sphere guidance for sufficient site space is 45m2 / person.
20,000 X 45m2/p = 900,000 m2
Let’s say our site is 900m x 1,000 m
1,000 m = 1 km
900 m = 0.9 km

## Slide 24: The building block approach
What about those firebreaks, distances between dwellings, etc. listed in the indicators?
These indicators are based on something called the ‘building block’ approach to site layout design.
In general, it works like this…
Notes: The presentation on ‘the building block approach’ is important because much of the camp planning guidance provided in Sphere is based on this model, although it is not specifically presented in the text.
Note the standard about privacy as well, and challenge the group to think through ways to achieve this in a dense camp situation. Take time to walk the participants through the steps carefully. Note that the placement of latrines and water points are also in line with the Sphere indicators. Remind the group that this is only one solution and that the ‘building blocks’ that may be used to design a large camp are many and varied. This solution is designed to show an approach only, not a ‘one size fits all solution’. The arrangement of the clusters will depend on many factors such as family size, available shelter options and traditional shelter habits of the people.

## Slide 25: The building block approach – master planning
Dwelling = 1 family ≃ 5 persons
Cluster = 16 families ≃ 80 persons
Block = 16 clusters ≃ 1,250 persons
Sector = 4 families ≃ 5,000 persons
Camp = 4 sectors ≃ 20,000 persons

## Slide 26: Dwelling
Example:
One tent Size = 17.5m2 = 1 dwelling
Shelter space per person = 3.5m2 (if there are 5 in the family)
5 M
3.5 M
Storage
Cooking/ Heating
Storage

## Slide 27: Cluster = 16 families
Sphere guidance notes call for “each shelter to open onto common space or a screened area for the use of the household instead of being opposite the entrance to another shelter.”
(page 257 of the 2011 Edition)
40m
45m
2m
ROAD
LATRINES

## Slide 28: Block = 16 clusters
6m between clusters
240m
180m
Zone for latrines

## Slide 29: Sector = 4 blocks
375 m
15 m between blocks
Water Point
455 m

## Slide 30: Camp = 4 sectors
1
2
3
4

## Slide 31: A typical camp layout
Sphere
Camp
1 kilometre
0.925 kilometre
Admin.
Support
Clinics, Dist Cntr.
Schools,
other support
Sector 1
Sector 2
Sector 3
Sector 4

## Slide 32: What does this mean for planning and programming?
If our study emergency population of 20,000 displaced has the demographic makeup described below, what programmatic impact does the information have on the provision of shelter materials to these people?
You have 3,750 pre-cut plastic sheets (4m x 5m)with metal eyelets at the edges for fastening with cord, people have access to light wooden poles. Heavy rain is possible within the next 2 weeks. Assume plenty of usable site area – no restriction.
  15,000 are in complete families, average family size = 6
  4,000 are minority population, average family size = 8
  1,000 are ex-fighters and child soldiers, all male, aged from 10-22 yrs. They claim no family attachment within the larger group.
Notes: This exercise dealing with distribution of plastic sheeting is very rich and should be carefully dissected after completion.
The message here is that math and sq. meters of plastic per person is only part of the story. The much more difficult and equally important part of shelter programs is the design of how to distribute materials in an equitable way when family sizes vary widely. The problem and the ‘textbook’ solution are provided at the end of this note. You may want to distribute the analysis to each of the participants after they work the exercise as a handout and explanation.
One possible solution to the problem is shown on the next slide.

## Slide 33: What is your basic plan?
What Sphere guidance will help you design your distribution program for these plastic sheets?
What is your basic plan?
Notes: The use of the « technical « indicators of 3.5m2 per person for shelter space is useful for this calculation.
The technical answer is described over the next several slides.
Remember that this is only one approach, and that there might be other appropriate solutions depending on the local norms and practices.
Other guidance is equally valuable such as involvement of the community, assessment of needs, and supporting local capacities…. Remember, no emergency operational response is purely ‘technical’.
Social and community norms are important as well as the maintaining of personal dignity and upholding the basic rights of those being assisted.

## Slide 34: One answer…
15,000 people average family size 6 means 2,500 families
1,000 soldiers
4,000 people average family size 8 means 500 families
Notes: This slide groups the population into different groups that can be provided with shelter while trying to keep families together. This is only the first step, make sure that the participants agree that this grouping represents the facts from the original question.

## Slide 35: One answer… (continued)
4m
5m
20 m2
4m
4m
4m
2.5m
2.5m
16 m2
Notes: This slide illustrates that the sheets of plastic, once made into shelters provide less area of coverage under roof than would be assumed by simply calculating the area of the plastic sheets flat.

## Slide 36: Textbook answer…
15,000 people average family size 6 means 2,500 families
  Give each family 1 sheet – each person gets 2.7m2 (16m2/6p = 2.66m2/p)
  2,500 sheets
1,000 soldiers
  Give every 5 soldiers 1 sheet. Each person gets 3.2m2 (16m2 5p = 3.2m2/p)
  200 sheets
4,000 people average family size 8 means 500 families
  Give each family 2 sheets – each person gets 4m2 (32m2/4p = 4.0m2/p)
  1,000 sheets
Keep 50 sheets for emergency reserve.
Notes: This slide shows the logic of distribution of sheets to families based on average family size.
It also suggests grouping the soldiers into groups of 5.
Arguments could be made to make these groups larger or smaller, but this choice does meet the Sphere guidance.
The families of average 8 people receive 2 sheets of plastic in order to meet the minimum of 3.5 m2 per person.

## Slide 37: Examples of possible distribution rules
But! Do not distribute according to ethnic group!
Rather set a rule – for example:
  Rule 1: Sheets are distributed to families first. 1 sheet for each family up to 6, 2 sheets for each family from 7-12 members.
  Rule 2: for those who may be grouped (same sex & age group) who are not in families, distribute 1 sheet for each 5.

## Slide 38: Some Sphere indicators for various NFIs…
“All women, girls, men, and boys have at least 2 full sets of clothing in the correct size…”
“Infants and children up to 2 years of age should also have a blanket in addition to appropriate clothing.”
(page 272 of the 2011 Edition)
Photo: actalliance.org
A boy receives a blanket in the Dada refugee camp in Kenya, 2012.

## Slide 39: Some Sphere indicators for commonly distributed NFIs
“Each household or group of four-to five individuals has access to two family-sized cooking pots with handles and lids, a basin for food preparation or serving, a kitchen knife, and two serving spoons.”
“All disaster-affected people have access to a dished plate, a spoon or other eating utensils and a mug or drinking vessel.”
(page 273 of the 2011 Edition)
Somalia, 2012. Photo: AP

## Slide 40: Exercise: Emergency Shelter Strategies
  In your groups, take time to consider your scenario.
  After establishing the probable needs, resources, and (making some assumptions) other contextual issues, consider the 5 emergency shelter options and choose the one you think most appropriate for your scenario.
  Be prepared to explain why you have made this choice, and what assumptions support your strategy.
Notes: This short exercise asks participants to match typical shelter response strategies to different emergency situations.
There are 7 scenarios provided. Choose in advance the scenarios most appropriate to your context and allocate one scenario to each group of 3 to 5 participants.
Ask participants to follow the instructions on the handout.
Each team must pick a strategy from the list (the group should agree) and then illustrate how this strategy might be monitored and or evaluated using the indicators from the Site and Shelter Chapter of the Sphere handbook.
The group action will need to be quite quick and reporting format should be very brief.
The conclusion of this exercise is simply that not all emergencies require emergency tent camps.
The 2004 edition of the Sphere handbook carefully orients the reader to the different shelter strategies available and presents camps as only one of several different available strategies, to be pursued only after other solutions.

## Slide 41: Remember!
The Humanitarian Charter and the technical chapters
should always come together.